## Slide 1
Lecture 1
Introduction
Sergei Savin, PhD
Innopolis University
Control Theory (Linear Control)
Slides design by Marko Pezer & Artem Bakhanov

## Slide 2: Topic of the Lecture
Control Theory (Linear Control)
Instructors
Grading
Introduction to Control
Single Input Single Output (SISO) Systems
Block Diagrams
From Linear DE to State Space Models
Slide 2

## Slide 3: Instructors
Control Theory (Linear Control)
Lecture Instructor:
Sergei Savin
Tutorial Instructor:
Sergei Savin
Labs Instructors:
Shamil Mamedov
Mike Ivanov
Oleg Balakhnov
Slide 3

## Slide 4: Grading
Control Theory (Linear Control)
Slide 4
Item | Percentage
Lab Quizzes | 10% (5x2%)
Homework | 50% (5x10%)
Mid-term Exam | 16%
Final Exam | 20%
Bonus Points | 4% (can be more)
Letter Grade | Percentage
A | 85-100
B | 70-84
C | 50-69
D | 0-49

## Slide 5: Process, System & Disturbance
Control Theory (Linear Control)
A process is any operation to be controlled. It can be chemical, biological, economical…
A system is a combination of components that act together and perform a certain objective.
A disturbance is a signal that adversely affects the value of the output of a system. It can be internal or external.
Slide 5

## Slide 6: Control & Control System
What is Control?
Control is a science.
Control is an engineering field.
Control is a process.
What is Control System?
Control System is an object.
Control system can be a model, a program, a circuit, or an electro-mechanical system.
Control Theory (Linear Control)

## Slide 7: Control System Examples
Industrial arms
Chemical plants
Self-driving cars
Slide 7
Control Theory (Linear Control)

## Slide 8: Single-Input Single-Output (SISO) Systems
Control Theory (Linear Control)
Single-Input Single-Output (SISO) System is a simple single variable control system with one input and one output.
Examples of SISO systems:
  Fan speed control
  Air conditioner temperature control
Slide 8

## Slide 9: Single-Input Single-Output (SISO) Systems
Consider the following ODE:
If we call an input, an output, then it is a SISO system.
Consider the following ODE:
Let us introduce output variable . Possibilities to choose it:
Control Theory (Linear Control)

## Slide 10: Open-Loop System vs. Closed-Loop System
Open-Loop System
no feedback
difficult to control output with accuracy
most of automates has open loop principle
Closed-Loop System
must have feedback
must have sensor on output
almost always negative
Control Theory (Linear Control)

## Slide 11: SISO Systems in Block Diagrams
Control Theory (Linear Control)
Slide 11
Controller
Controlled
Process
Input
Output
Open Loop System

## Slide 12: State-Space Models
Control Theory (Linear Control)
State-Space Representation is a mathematical model of a physical system as a set of input, output and state variables related by first-order differential equations or difference equations.
General form of State-Space representation:
Slide 12

## Slide 13: Single-Input Single-Output (SISO) Systems
Classic example (second order mass-spring system):
State-space model:
Let us set:
Now we will have:
Control Theory (Linear Control)

## Slide 14: Additional Materials about State-Space Models
From ODE to State Space
Who wants to learn more?
Control Theory (Linear Control)
https://www.youtube.com/watch?v=HGFZ_fl3C0c
https://www.youtube.com/playlist?list=PLn8PRpmsu08podBgFw66-IavqU2SqPg_w

## Slide 15: Linearity
Control Theory (Linear Control)
A system is linear with respect to its inputs and output
if and only if superposition holds:
So, if is the response of to (), and is the response of to (), then the response to is
Slide 15

## Slide 16
The End
Do you have any questions?